## Slide 1: Project Work
PROJECT EXPERIS
KILOMETRO ROSSO – 21/05/2018
Running a maze
Marco Stucchi

## Slide 2: Getting the source code
PROJECT EXPERIS
Online repositories

## Slide 3: Github repository
https://github.com/experisABB

## Slide 4: SourceTree
GIT GUI for Windows & MAC
https://www.sourcetreeapp.com/ to download specific version
Installation
  Accept License Agreement
  Login with Atlassian account (don’t have an account ? Sign up for one)
  Download and Install tools (Git + Mercurial)
  Use default ignore file
  Skip SSH key

## Slide 5: SourceTree
Connecting to Github

## Slide 6: SourceTree settings
Source Path / Destination Path
Get the Source Path URL from the «Clone or download» menu in Github repository
Set the Destination Path as desired on the local machine

## Slide 7: SourceTree
Select Starting Tag
Double click on the «v1.0-original» tag
The empty circle indicates the checkout on the selected Tag

## Slide 8: Demo Application
PROJECT EXPERIS
STM32F429I Discovery Board

## Slide 9: Getting the Project
Project file: MEMS_Example.uvproj
Can be found under {Destination Path}
MDK-ARM Project

## Slide 10: Project v1.0-original – ST Microelectronics original code
Getting familiar with the code
Release: v1.0-original

## Slide 11: Possible bug ?
Check the behaviour
Occasional glitch in the detected direction
What can we do ?
Let’s instrument our code..
..and check the axis rotation in a buffer of 256 values
..an array of values taken from Buffer[1]

## Slide 12: Run-time debugging
Make the correct settings

## Slide 13: Run-time debugging (timer_ms)
Insert variable that counts ms
Attach to specific ISR (which one ?)
Check timer interrupt interval
Execute Gyro reading on timer change
Release: v1.0.2

## Slide 14: Buffer debugging
Anything strange ?

## Slide 15: Additional debug
Check the behaviour
Check the raw data to see if there is a match
Let’s instrument our code..
..and check the raw axis rotation in a buffer of 256 values
..an array of values taken from RawData[1]
Let’s align in two memory windows and compare
What’s the relation between the two buffers ?
Release: v1.0.3

## Slide 16: Raw Data
Wrong scaling factor ?

## Slide 17: Bug found
Typecast confusion
Release: v1.1

## Slide 18: Maze
PROJECT EXPERIS
STM32F429I Discovery Board

## Slide 19: Orientation
State Machine
Maze_GetNewOrientation
Return bool. true = Orientation updated
Parameters : float XSpeed, float Yspeed
Xspeed = Buffer[0], Yspeed = Buffer[1]
Xspeed  Up, Down
Yspeed  Left, Right

## Slide 20: Basic drawing
ST Disco driver
Based on ILI9341 single chip driver
ST Micro libraries (no emWin)
Basic functions:
  LCD_SetTextColor
  LCD_DrawRect
  LCD_FillTriangle

## Slide 21: Available Colors
ST Disco driver
0x0000 Black
0xFFFF White
0x051F Light Blue
0xF800 Red

## Slide 22: Draw border and Direction
Center in the middle of the display
Outer size = 198
Arrow size (base = 36, height = 12)

## Slide 23: Draw border and Direction
Maze structures
Release: v1.2.2

## Slide 24: Add a ball in the maze
New files: ball.c/ball.h
Color Red (0xF800)
Add cinematic
  Acceleration (e.g. 60 pixels/s^2)
  Deceleration (e.g. 15 pixels/s^2)
  Speed (e.g. speed max = 120 pixel/s)
  Position (manage borders)
  Radius = 6 px
  On border impact: rebound
  Semi-elastic rebound

## Slide 25: Add a ball in the maze
New functions
Ball_Adjust_aVS(eOrientation)
Maze_DrawTheBall( uint x, uint y)
New class, Ball
float x_accel, y_accel
float x_speed, y_speed
Float x_position, y_position
Used graphic function:
LCD_DrawFullCircle(ushort X, Y, radius)
Release: v1.2.3

## Slide 26: Improve the border check
Let’s think about something different
New algorithm suitable for a maze
Req: maze knowledge not required
Any ideas ?
Readback from the LCD memory !!
Take a look at the library
New functions:
  Ball_closeToWall ( which direction ?)
  Ball_CheckProximity
Release: v1.2.4

## Slide 27: A Maze, finally
Let’s start drawing a maze
Different automatic maze algorithms are possible
Recursive Division:
  Divide in 4 rooms
  Make 3 openings
  Iterate

## Slide 28: A Maze, finally
Let’s start drawing a maze
Let’s start with something like this:
  Single iteration
  Divide the screen in 4 rooms
  Make 3 holes wherever you want
The new proximity algorithm should already work
New function: Maze_DrawInner
Possible cinematic adjustment (e.g. deceleration)
Release: v1.2.5

## Slide 29: There’s a hole in my maze
Let’s place a destination for the ball wandering
Hole radius = 12 pixels
Add the hole position to the maze structure
New function: Maze_DrawHole
Release: v1.2.6

## Slide 30: Final touches
Avoid bouncing into the hole
When the ball enters the hole, it is trapped
And more….
  Real games need a time
  Store best times in a non volatile memory
  You name it..
Release: v1.2.10